## Slide 1: Building reliable, high-performance communication systems from components
Xiaoming Liu, Christoph Kreitz, Robbert van Renesse, Jason Hickey, Mark Hayden, Ken Birman, Bob Constable
(shepherd: Peter Lee)
Cornell, Caltech, Compaq (CMU, Cedilla)

## Slide 2: Why software components?
Ease design and development
Tuning to environment
Customization to user app
Extensibility
Verification and robustness
Notes: VLSI designers long used this approach successfully.

## Slide 3: Why not?
Configuration is hard
Performance is bad
  Abstraction barriers
  Poor locality
  Redundant code
Not reliable
Not faster
Notes: Systems of two decades ago are just as fast and reliable as today’s systems, in spite of much faster hardware.

## Slide 4: Group Communication
Network
Notes: Set of machines cooperating towards a common goal.

## Slide 5: History
V
Ensemble
Isis
Horus
Multicast
Membership
CATOCS
Layers
Protocols
ML
Formal methods
Notes: Horus: x-kernel influence

## Slide 6: Specification
Concrete (ML)
Implementation
Properties
(English)
code of a layer
logical
predicates
Notes: Hard to go between two forms of specification.

## Slide 7: Specification
Abstract Spec
Concrete (ML)
Implementation
Properties
(English)
refinement
proof
(I/O Automata)
Notes: Abstract Spec: behavioral, global state
Refinement: design choices (e.g., token or sequencer)

## Slide 8: Abstract IOA specification of totally ordered multicast
S: array[integer] of message
next: integer
deliv: array[process] of integer
action Multicast(m) { S[next++] := m; }
action Deliver(p, m)
precond: deliv[p] < next && m == S[deliv[p]]
{ deliv[p]++; }
global
state
Notes: Specification of a reliable totally ordered network. Formal semantics, yet easy to read and write by programmers. Easy to see that it provides totally ordered delivery. It doesn’t say much about how to implement it, leaving freedom to the implementer.

## Slide 9: Layer correctness
abstract FIFO
network spec
abstract Total
Order network
spec
Hickey, Lynch, Van
Renesse, TACAS’99
network + layer == network++
Token layer on each CPU
Notes: Once you have an implementation, you can prove it correct, as we’ve done for a particular implementation of total order. We found a subtle bug!

## Slide 10: Stack correctness
Seqno layer
FIFO
total
unreliable
Token layer
For example:
Seqno
Token
Notes: Once you’ve proved a few layers correct, it’s relatively easy to build a correct stack.

## Slide 11: Efficiency?
Ensemble stacks have many layers, improving clarity, but inefficient.
5 optimization techniques:
  Avoiding (in-line) garbage collection
  Avoiding marshaling
  Delaying non-critical message processing
  Identifying common paths
  Header compression
Notes: First three techniques independent of layering. Last two beyond capabilities of compiler optimizations, and has involved hand-optimization or significant annotation of code. This is a difficult and error-prone process.

## Slide 12: A protocol layer is a function!
old state
new state
input event
output events
layer
Notes: A protocol layer is a function that takes the current state and an event as input, and produces a new state and zero or more output events. Those events, in turn, are fed to other layers.

## Slide 13: (off-line) partial evaluation
Common Case
Predicate
original code
Specialized
code
Hacker +
Formal person
NuPrl
layer
Notes: NuPrl is a formal tool that can manipulate formal specifications. Both the programmer of a protocol layer, as well as a NuPrl expert are necessary to do the manipulations. An example of a CCP is “the sequence number on the incoming message is the one that is expected”. In other words, the common case is that no messages are lost, re-ordered, or duplicated. Other examples are: “the message is a data message”, “the message is not fragmented”, etc.

## Slide 14: Two-phase optimization
Programmer
Formal
User
code
CCP
bypass
function
Off-line
On-line
TT
TT
Notes: TT is “type theory”, the input language to NuPrl. The partial evaluation is done off-line. The composition is also done by NuPrl, but can be done fully automatically. A translator translates TT back into ML.

## Slide 15: Header compaction
T_Data
T_Data
seqno
T_Last
Hash
seqno
Less space
Faster processing
Notes: As NuPrl generates code, it will notice that certain header values are constant. These constants are hashed together, saving space and processing overhead.

## Slide 16: Architecture (deliver only)
Network
Application
?
generated bypass
original stack
CCP (e.g., hdr.seq = win.lo)
Transport driver
(marshaling, device
independence)
Notes: After NuPrl generates the bypass code, it needs to be configured into the system. The CCPs are combined to decided whether a particular message can go through the bypass code or not. A Transport module is used in Ensemble to marshal messages and to provide network device independence.

## Slide 17: Architecture
Network
Application
?
?
generated bypass
original stack
CCP
Transport driver
(marshaling, device
independence)
Notes: After NuPrl generates the bypass code, it needs to be configured into the system. The CCPs are combined to decided whether a particular message can go through the bypass code or not. A Transport module is used in Ensemble to marshal messages and to provide network device independence.

## Slide 18: Performance
Three different versions:
  Original (ORIG)
  Hand-optimized (HAND)
  Machine-optimized (MACH)
300 MHz UltraSparc/Solaris 2.6
OCaml 2.0 native code compiler
Notes: We measured the performance on three different versions of Ensemble.

## Slide 19: Code latency (sec)
 | 10 layer |  | 4 layer stack |  | 
 | ORIG | MACH | ORIG | MACH | HAND
Down Stack | 20 | 9 | 13 | 2 | 2 + 4
Down Transport | 27 | 8 | 6 | 6 | 
Up Transport | 20 | 7 | 8 | 7 | 6 + 2
Up Stack | 14 | 8 | 10 | 4 | 
Total | 81 | 32 | 37 | 19 | 14
(See paper for CPU cycles and TLB misses)
Notes: Paper contains detailed information.

## Slide 20: Lessons learned
Design with formalization in mind
Use small, but not too small components
Use a language with formal semantics
Use IOA as a specification language
Use formal tool with in-house expertise
Notes: If you’re interested in building a robust system, and willing to use formal methods, …

## Slide 21: Final remarks
See CD or Web for code samples, links to all code, as well as how to reproduce our results
Still working on a machine-generated proof of correctness
Notes: Thank you for your attention.